## Slide 1: IMSE 802 Supply Chain Operations and Decision Making
Lecture 3
Supply Chain Models

## Slide 2: Supply Chain Models
Supply Chain Models
Transportation Model – LP
Product Mix Model – LP
Warehouse and Inventory Level Optimization Model Example

## Slide 3: Supply Chain Decision Levels
Strategic
  Long-term decisions and objectives
  High-level decisions, i.e., facility location, supplier selection, supply chain design, etc.
Tactical
  Midterm decisions concerning issues such as transportation planning, distribution planning, etc.
Operational
  Short term decisions which are concerned with daily managerial activities such as inventory planning, demand planning, forecasting, etc.

## Slide 4: Supply Chain Models
How do we analytically address planning and execution at each of these levels?
What tools can we use to best manage the supply chain overall and the individual elements of the supply chain?
What type of IT infrastructure do we need to support these processes?

## Slide 5: Supply Chain Models
A variety of optimization and supply chain models exist that can be used to assist us in our decision making.
Much research is done in a variety of these areas
System exist that are implemented to assist us in these decision making processes.

## Slide 6: Supply Chain Models
Decisions need to be supported by robust tools to enable managers to evaluate the impact of their decisions prior to making them.
System modelling is used to model the real system.
These models can be mathematical models or simulation models.
System complexity can make mathematical models difficult to implement in practice.

## Slide 7: Supply Chain Models
The interaction between supply chain components (i.e., manufacturing plants, retailers, warehouses, and distribution centers) defines its complicated behavior and is very difficult to build analytical expression that describes it precisely.
Simulation is one of the most successful tools for analyzing supply chain processes.

## Slide 8: Supply Chain Models
Optimization Methods in Supply Chain Applications: a Review, Conference Paper, Dublin Institute of Technology, Amr Arisha and Waleed Abo-Hamad, 12th Annual Conference of the Irish Academy of Management, Galway Mayo Institute of Technology, Galway, 2-4 September 2009.

## Slide 9: Supply Chain Models
Optimization Methods in Supply Chain Applications: a Review, Conference Paper, Dublin Institute of Technology, Amr Arisha and Waleed Abo-Hamad, 12th Annual Conference of the Irish Academy of Management, Galway Mayo Institute of Technology, Galway, 2-4 September 2009.

## Slide 10: Supply Chain Models
Optimization Methods in Supply Chain Applications: a Review, Conference Paper, Dublin Institute of Technology, Amr Arisha and Waleed Abo-Hamad, 12th Annual Conference of the Irish Academy of Management, Galway Mayo Institute of Technology, Galway, 2-4 September 2009.

## Slide 11: Supply Chain Models
General Problem Formation
  Optimize fi(x) i = 1,…,I
  Subject to gj(x) <=0 j = 1,…,J
  hk(x) = 0 k = 1,…,K
  Where fi(x) is the objective function i, x represents the decision variable vector and gi(x), hi(x) are the set of inequality and equality constraints

## Slide 12: Supply Chain Models
Challenges
  Obtaining a true mathematical description of fi(x) is not attainable
  Traditional optimization is not adequate for complex problems
  There are typically multiple objectives that must be optimized concurrently.
  A large number of variables are encountered with large ranges

## Slide 13: Supply Chain Models
Optimization Methods in Supply Chain Applications: a Review, Conference Paper, Dublin Institute of Technology, Amr Arisha and Waleed Abo-Hamad, 12th Annual Conference of the Irish Academy of Management, Galway Mayo Institute of Technology, Galway, 2-4 September 2009.

## Slide 14: Supply Chain Models
https://www.sciencedirect.com/science/article/pii/S037722171300787X

## Slide 15: Research Survey – Dimensions of SCM
(1) The primary actor that is the focus of the study
(2) The organizational level of analysis ranging from internal functions to broad macro-economic focus;
(3) The SCOR process covered in the model, and
(4) The functional application area in the model (e.g. SCM, logistics, or product development).
https://www.sciencedirect.com/science/article/pii/S037722171300787X

## Slide 16: Research Survey - Modeling
https://www.sciencedirect.com/science/article/pii/S037722171300787X

## Slide 17: Supply Chain Models
Many methods exist
Many parameters need to be modeled in the supply chain
Results must represent real-world operations to be useful
Over-complication may make using the model difficult

## Slide 18: Optimization Models
Linear Programming (LP) Models in Supply Chain Management
  LP models allow us to model a component of the supply chain to optimize the objectives and constrain the solution based on available resources
  LP models can be used in a variety of areas of the supply chain

## Slide 19: LP Models Applying to Supply Chains
Type of Model | Variables | Function to Optimize | Typical Constraints
Product Mix | Number of products to produce | Maximize contribution to profit | Resource limits, such as time, labor, material; maximum or minimum quantities
Blending | Amount of materials to combine to produce one unit of product | Minimizing cost | Resource limits; demand requirements
Production line scheduling | Sequence of production | Minimize cost | Resource limits; time requirements
Inventory | Number of inventory items to order by period | Minimize cost (sum of production and inventory) | On-hand minimums by time period; inventory balance equations
Transportation | Assign sources for distribution of goods to demands | Minimize cost | Capacity limits at sources; demand requirements
Assignment | Assign sources of resources to tasks | Minimize cost | Conventional sources and demand capacities equal 1

## Slide 20: LP Models with Supply Chains
Components
  Variables – Items that can be varied in order to improve or positively contribute to the objective
  Functions in terms of variables – mathematical statements measuring something in terms of the variables
  Limits to Functions – Limitations imposed on the problem or environment

## Slide 21: LP Models with Supply Chains
Components
  Focus on the decision to be made
  Focus on things that are within the decision-maker’s control
  Identify the objective of the decision
  Set limits and insure that all limits are captures

## Slide 22: Example – Shipping Schedule
Deliver petroleum from refineries to depots.
Refineries
  Houston
  Corpus Christi
  Fort Worth
Depots
  San Antonio
  Bryan
  El Paso

## Slide 23: Example – Shipping Schedule
System Parameters
Refinery | Capacity (Thousand gallons) | Depot | Requirements (thousand gallons)
Houston | 150 | San Antonio | 200
Corpus Christi | 100 | Bryan | 120
Fort Worth | 250 | El Paso | 180

## Slide 24: Example – Shipping Schedule
Shipping Unit Costs
Source | (S) San Antonio | (B) Bryan | (E) El Paso | Supply (thousand gallons)
(H) Houston | $200 | $90 | $50 | 150
(C) Corpus Christi | $60 | $100 | $180 | 100
(F) Fort Worth | $20 | $150 | $120 | 250
Demand (thousand gallons) | 200 | 120 | 180 | 500

## Slide 25: Example – Shipping Schedule
Objective function
  Minimize transportation costs
  Coefficients are unit costs
Variables
  Quantity shipped that day of over the indicated route
Constraints
  Quantity shipped out of each refinery is less than or equal to the refinery’s capacity
  Quantity received by the depot is at least as much supply as is needed to cover demand.

## Slide 26: Example – Shipping Schedule
Formulation
  Minimize = 200 HS + 90 HB + 50 HE + 60 CS + 100 CB + 180 CE + 20 FS + 150 FB + 120 FE
  Subject to:
    HS + CS + FS >= 200
    HB + CB + FB >= 120
    HE + CE + FE >= 180
    HS + HB + HE <=150
    CS + CB + CE <=100
    FS + FB + FE <=250
    HS, HB, HE, CS, CB, CE, FS, FB, FE >= 0

## Slide 27: Example Shipping - Schedule
Excel Formation
 |  | HS | HB | HE | CS | CB | CE | FS | FB | FE | Function |  | Limit
 | Quantities | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 
 | Costs | 200 | 90 | 50 | 60 | 100 | 180 | 20 | 150 | 120 |  |  | 
Supplies | Houston | 1 | 1 | 1 |  |  |  |  |  |  | 0 | <= | 150
 | Corpus Christi |  |  |  | 1 | 1 | 1 |  |  |  | 0 | <= | 100
 | Fort Worth |  |  |  |  |  |  | 1 | 1 | 1 | 0 | <= | 250
Demands | San Antonio | 1 |  |  | 1 |  |  | 1 |  |  | 0 | >= | 200
 | Bryan |  | 1 |  |  | 1 |  |  | 1 |  | 0 | >= | 120
 | El Paso |  |  | 1 |  |  | 1 |  |  | 1 | 0 | >= | 180

## Slide 28: Example Shipping - Schedule
Excel Formation – Showing Cell Formulas
 |  | HS | HB | HE | CS | CB | CE | FS | FB | FE | Function |  | Limit
 | Quantities | 0 | 0 | 150 | 0 | 100 | 0 | 200 | 20 | 30 | =SUMPRODUCT($C$2:$K$2,C3:K3) |  | 
 | Costs | 200 | 90 | 50 | 60 | 100 | 180 | 20 | 150 | 120 |  |  | 
Supplies | Houston | 1 | 1 | 1 |  |  |  |  |  |  | =SUMPRODUCT($C$2:$K$2,C4:K4) | <= | 150
 | Corpus Christi |  |  |  | 1 | 1 | 1 |  |  |  | =SUMPRODUCT($C$2:$K$2,C5:K5) | <= | 100
 | Fort Worth |  |  |  |  |  |  | 1 | 1 | 1 | =SUMPRODUCT($C$2:$K$2,C6:K6) | <= | 250
Demands | San Antonio | 1 |  |  | 1 |  |  | 1 |  |  | =SUMPRODUCT($C$2:$K$2,C7:K7) | >= | 200
 | Bryan |  | 1 |  |  | 1 |  |  | 1 |  | =SUMPRODUCT($C$2:$K$2,C8:K8) | >= | 120
 | El Paso |  |  | 1 |  |  | 1 |  |  | 1 | =SUMPRODUCT($C$2:$K$2,C9:K9) | >= | 180

## Slide 29: Example Shipping - Schedule
Excel Formation
 |  | HS | HB | HE | CS | CB | CE | FS | FB | FE | Function |  | Limit
 | Quantities | 0 | 0 | 150 | 0 | 100 | 0 | 200 | 20 | 30 | 28100 |  | 
 | Costs | 200 | 90 | 50 | 60 | 100 | 180 | 20 | 150 | 120 |  |  | 
Supplies | Houston | 1 | 1 | 1 |  |  |  |  |  |  | 150 | <= | 150
 | Corpus Christi |  |  |  | 1 | 1 | 1 |  |  |  | 100 | <= | 100
 | Fort Worth |  |  |  |  |  |  | 1 | 1 | 1 | 250 | <= | 250
Demands | San Antonio | 1 |  |  | 1 |  |  | 1 |  |  | 200 | >= | 200
 | Bryan |  | 1 |  |  | 1 |  |  | 1 |  | 120 | >= | 120
 | El Paso |  |  | 1 |  |  | 1 |  |  | 1 | 180 | >= | 180

## Slide 30: Example Shipping - Schedule
Excel Formation
 |  | HS | HB | HE | CS | CB | CE | FS | FB | FE | Function |  | Limit
 | Quantities | 0 | 0 | 150 | 0 | 100 | 0 | 200 | 20 | 30 | 28100 |  | 
 | Costs | 200 | 90 | 50 | 60 | 100 | 180 | 20 | 150 | 120 |  |  | 
Supplies | Houston | 1 | 1 | 1 |  |  |  |  |  |  | 150 | <= | 150
 | Corpus Christi |  |  |  | 1 | 1 | 1 |  |  |  | 100 | <= | 100
 | Fort Worth |  |  |  |  |  |  | 1 | 1 | 1 | 250 | <= | 250
Demands | San Antonio | 1 |  |  | 1 |  |  | 1 |  |  | 200 | >= | 200
 | Bryan |  | 1 |  |  | 1 |  |  | 1 |  | 120 | >= | 120
 | El Paso |  |  | 1 |  |  | 1 |  |  | 1 | 180 | >= | 180

## Slide 31: Product Mix Example
The features of a product mix problem are that there is a collection of products competing for a finite set of resources.
If there are m resources and n products, then there m rows by n columns of coefficients
The coefficient in row i, column j, is the number of units of resource i used by each unit of product j.

## Slide 32: Product Mix Example
Associated with each product is a profit contribution
Associated with each resource is an availability.
The objective is to find how much to produce of each product (i.e., the mix) to maximize profits subject to not using more of each resource than is available.

## Slide 33: Product Mix Example
A factory produces four different types of wood paneling.
Each type of paneling is made by gluing and pressing together a different mixture of pine and oak chips.
The following table summarizes the required amount of gluing, pressing, and mixture of wood chips required to produce a pallet of 50 units of each type of paneling:

## Slide 34: Product Mix Example
 | Resources Required per Pallet of Paneling Type |  |  | 
 | Tahoe | Pacific | Savannah | Aspen
Glue (quarts) | 50 | 50 | 100 | 50
Pressing (hours) | 5 | 15 | 10 | 5
Pine chips (pounds) | 500 | 400 | 300 | 200
Oak chips (pounds) | 500 | 750 | 250 | 500

## Slide 35: Product Mix Example
In the next production cycle, you have 5,800 quarts of glue; 730 hours of pressing capacity; 29,200 pounds of pine chips; and 60,500 pounds of oak chips available. Further assume that each pallet of Tahoe, Pacific, Savannah, and Aspen panels can be sold for profits of $450, $1,150, $800, and $400, respectively.

## Slide 36: Product Mix Example
Use the symbol X1 for the number of Tahoe pallets produced, X2 for the number of Pacific pallets produced, and X3 for the number of Savannah pallets produced, and X4 for the number of Aspen pallets produced, the objective (calculating total profit) is:
Maximize: 450 X1 + 1150 X2 + 800 X3 + 400 X4

## Slide 37: Product Mix Example
A pallet of each type of panel requires a certain amount of glue, pressing, pine chips, and oak chips.
The amount of resources used (calculated by the left hand side of each constraint) depends on the mix of products built
We have a limited amount of each type of resource available (corresponding to the constraint right hand side values).

## Slide 38: Product Mix Example
The constraints for this problem are expressed as follows:
Subject to:
  50 X1 + 50 X2 + 100 X3 + 50 X4 <= 5800 (Glue)
  5 X1 + 15 X2 + 10 X3 + 5 X4 <= 730 (Pressing)
  500 X1 + 400 X2 + 300 X3 + 200 X4 <= 29200 (Pine chips)
  500 X1 + 750 X2 + 250 X3 + 500 X4 <= 60500 (Oak chips)

## Slide 39: Product Mix Example
Since the number of products built cannot be negative, we'll also have non-negativity conditions on the variables:
X1, X2, X3, X4 >= 0.

## Slide 40: Product Mix Example
To define an optimization model in Excel follow these steps:
  Organize the data for your problem in the spreadsheet in a logical manner.
  Choose a spreadsheet cell to hold the value of each decision variable in your model.
  Create a spreadsheet formula in a cell that calculates the objective function for your model.
  Create a formulas in cells to calculate the left hand sides of each constraint.
  Use the dialogs in Excel to tell the Solver about your decision variables, the objective, constraints, and desired bounds on constraints and variables.
  Run the Solver to find the optimal solution.
Create a spreadsheet that communicates its purpose in a clear and understandable manner.

## Slide 41: Product Mix Example

## Slide 42: Product Mix Example
 | Panel Type |  |  |  |  |  | 
 | Tahoe | Pacific | Savannah | Aspen |  |  | 
Pallets | 0 | 0 | 0 | 0 | Total Profit |  | 
Profit | $450 | $1,150 | $800 | $400 | $0 |  | 
 | Resources Required per Pallet of Paneling Type |  |  |  | Used | Available | Units
Glue | 50 | 50 | 100 | 50 | 0 | 5800 | quarts
Pressing | 5 | 15 | 10 | 5 | 0 | 730 | hours
Pine chips | 500 | 400 | 300 | 200 | 0 | 29200 | pounds
Oak chips | 500 | 750 | 250 | 500 | 0 | 60500 | pounds

## Slide 43: Product Mix Example
The profit for each pallet of panels is Tahoe, $450, Pacific, $1,150, Savannah, $800, and Aspen, $400.
The objective function is computed in cell F5 as: =SUMPRODUCT(B5:E5,B4:E4)

## Slide 44: Product Mix Example
In cells B8:E11, we've entered the amount of resources needed to produce a pallet of each type of panel.
For example, the value 15 in cell C9 means that 15 hours of pressing is required to produce a pallet of Pacific style panels.

## Slide 45: Product Mix Example
The formulas to compute the amount of resources used based on the solution are entered in cells F8 – FF11. For example, the formula for cell F8: =SUMPRODUCT($B$4:$E$4,B8:E8)
In cells G8:G11, we've entered the available amount of each type of resource (corresponding to the right hand side values of the constraints).
This allows us to express the constraints shown earlier as: F8:F11<=G8:G11
This is equivalent to the four constraints: F8<=G8, F9<=G9, F10<=G10, and F11<=G11.

## Slide 46: Product Mix Example
We can enter this set of constraints directly in the Solver dialogs along with the non-negativity conditions:
B4:E4 >= 0

## Slide 47: Product Mix Example
Using Solver
  In the By Changing Variable Cells edit box, we type B4:E4 or select these cells with the mouse
  To add the constraints, we click on the Add button in the Solver Parameters dialog and select cells F8:F11 in the Cell Reference edit box (the left hand side), and select cells G8:G11 in the Constraint edit box (the right hand side); the relation <= is OK.

## Slide 48: Product Mix Example
Showing Formulas
 | Panel Type |  |  |  |  |  | 
 | Tahoe | Pacific | Savannah | Aspen |  |  | 
Pallets | 0 | 0 | 0 | 0 | Total Profit |  | 
Profit | 450 | 1150 | 800 | 400 | =SUMPRODUCT($B$4:$E$4,B5:E5) |  | 
 | Resources Required per Pallet of Paneling Type |  |  |  | Used | Available | Units
Glue | 50 | 50 | 100 | 50 | =SUMPRODUCT($B$4:$E$4,B8:E8) | 5800 | quarts
Pressing | 5 | 15 | 10 | 5 | =SUMPRODUCT($B$4:$E$4,B9:E9) | 730 | hours
Pine chips | 500 | 400 | 300 | 200 | =SUMPRODUCT($B$4:$E$4,B10:E10) | 29200 | pounds
Oak chips | 500 | 750 | 250 | 500 | =SUMPRODUCT($B$4:$E$4,B11:E11) | 60500 | pounds

## Slide 49: Product Mix Example

## Slide 50: Product Mix Example
Using Solver
  To find the optimal solution, we click on the Solve button.
  This means that we should build
    23 pallets of Tahoe panels
    15 pallets of Pacific panels
    39 pallets of Savannah panels
    0 pallets of Aspen panels.
  This results in a total profit of $58,800

## Slide 51: Product Mix Example
Answer Report
  We can generate an Answer Report by clicking on "Answer" in the Reports list box.
  This report shows the original and final values of the objective function and the decision variables, as well as the status of each constraint at the optimal solution.
  The constraints on glue, pressing, and pine chips are binding and have a slack value of 0.
  There were 28,000 pounds of oak chips left over.
  If we could obtain additional glue, pressing capacity, or pine chips we could further increase total profits.

## Slide 52: Product Mix Example
Answer Report
Objective Cell (Max) |  |  |  |  |  |  | 
 | Cell | Name | Original Value | Final Value |  |  | 
 | $F$5 | Profit Total Profit | $58,800 | $58,800 |  |  | 
Variable Cells |  |  |  |  |  |  | 
 | Cell | Name | Original Value | Final Value | Integer |  | 
 | $B$4 | Pallets Tahoe | 23 | 23 | Contin |  | 
 | $C$4 | Pallets Pacific | 15 | 15 | Contin |  | 
 | $D$4 | Pallets Savannah | 39 | 39 | Contin |  | 
 | $E$4 | Pallets Aspen | 0 | 0 | Contin |  | 
Constraints |  |  |  |  |  |  | 
 | Cell | Name | Cell Value | Formula | Status | Slack | 
 | $F$8 | Glue Used | 5800 | $F$8<=$G$8 | Binding | 0 | 
 | $F$9 | Pressing Used | 730 | $F$9<=$G$9 | Binding | 0 | 
 | $F$10 | Pine chips Used | 29200 | $F$10<=$G$10 | Binding | 0 | 
 | $F$11 | Oak chips Used | 32500 | $F$11<=$G$11 | Not Binding | 28000 | 
 | $B$4 | Pallets Tahoe | 23 | $B$4>=0 | Not Binding | 23 | 
 | $C$4 | Pallets Pacific | 15 | $C$4>=0 | Not Binding | 15 | 
 | $D$4 | Pallets Savannah | 39 | $D$4>=0 | Not Binding | 39 | 
 | $E$4 | Pallets Aspen | 0 | $E$4>=0 | Binding | 0 | 

## Slide 53
Warehouse and Inventory Level Optimization Model

## Slide 54: General Modeling Overview
1. Solving the Right Problem
(Find out what you know and don’t know)
Preliminary Fact Finding
Group Decision Making
Metrics Identification to Measure Criteria
Data Sources Identification to Support Metrics
2. Measuring Success in Accomplishing the Objectives (their Metrics)
3. What is the Decision to be Made?
Automated Data Sources
Expert Opinions
Surveys/Data Gathering
4. Data Mining and Statistical Analysis – (Look at the data first. The answer may be obvious and you don’t need further analysis.)
5. Selection of Best Decision Methodologies
Interaction Between Model Structure and Data to Support Model.
7. Model to Support Decision Process
8. Insure Decisions that Support the Objectives with Appropriate Measures of Success
Automate the Decision Process
Ability for “What - If” and Sensitivity Analysis
May require re-definition
Translate goals and objectives into criteria or measures of success
6. Select the Best Method that the Data will Support and Imbed in a Dynamic Model.

## Slide 55: General Modeling Overview
Key aspects of this process are helpful in developing models that result in real-world models
  Solve the right problem
  Measure success in accomplishing objectives
  What is the decision to be made?
  Data mining and statistical analysis
  Selection of the best decision methodology
  Select the method that the data will support and embed it in a dynamic model
  Model to support the decision process
  Insure the methods support the objectives with appropriate measure of success

## Slide 56: Warehouse and Inventory Level Optimization Study
System Overview
The two objectives in the problem were to minimize cost of operations and to maximize customer satisfaction (or minimize customer dissatisfaction)
The problem was to determine the size of the warehouse needed for a brewing company.
On the surface, this appears to be a relatively simple problem
To solve this is a much more complicated question that includes issues such as customer demand, brewing and packaging variability, safety stock levels and product preferences.
To develop a model, we need to define the real problem, identify available data, analyze the data and statistical analysis, select the appropriate modeling methodologies and integrate these components into a general decision model.

## Slide 57: Warehouse and Inventory Level Optimization Study
General Concept of the System
The general concept of the system is to establish the safety stock and inventory level required to support the desired service level to the wholesalers.
As statistical analysis was done on the production forecast and actual production and sales to measure their variability for establishing safety stock requirements.
Once this is done, the production of products is measured as they flow through brewing, packaging, warehousing and distribution to dynamically determine the optimal Full Goods Days Inventory as an output of the system.

## Slide 58: Warehouse and Inventory Level Optimization Study
General Concept of the System
To accomplish this, three major steps must be accomplished:
  Analyze the demand and determine the optimal safety stock required to support a desired service level.
  Perform a weekly trade-off analysis between cost and out-of-stock lost sales to refine the safety stock requirements when all demand cannot be met. (MODM model)
  Follow the flow through the entire process with an expert system to understand how the inventory fluctuates on individual shifts.

## Slide 59: Warehouse and Inventory Level Optimization Study
Safety Stock Determination Overview
Data was analyzed to determine the variation in what was forecast and what was actually produced and the variation in sales.
A combined variation in production and sales is required for the analysis.
Because of the high dependency of brewing with packaging and data issues, both were identified as production variability.
Data was used to try to match forecast with actual data. This was done with a fair amount of time and some difficulty.

## Slide 60: Warehouse and Inventory Level Optimization Study
Safety Stock Determination Overview
The variability being captured was unplanned variability in production and sales. Safety stock covers unplanned variability. Buffer stock covers planned variability.
We needed to measure the desired production amounts and the actual production amounts.
Orders and production were matched at three weeks out. Prior to this, orders drive production, after this, production drives orders.

## Slide 61: Warehouse and Inventory Level Optimization Study
Safety Stock Determination Overview
In this environment, the following general statistical analysis was selected.
1. Capture sales across all wholesalers to develop the sales distribution by product and container and calculate σ * the variability in sales.
2. Match the forecast production for each product with the production three weeks later. Fit a least squares model that predicts actual production from forecast production.
Calculate the expected production AP as a function of forecasted production.

## Slide 62: Warehouse and Inventory Level Optimization Study
Safety Stock Determination Overview
In this environment, the following general statistical analysis was selected.
4. Calculate σ* the variability of production for each product.
5. Calculate the combined variability of production and sales.
z = σ 2+ σ*2
6. With this estimate of production and sales variability, the distribution can then be developed and the desired safety stock levels for each product determined. An acceptable frequency of stock-outages for each product P(z > zc) where zc is the combined safety stock of the wholesalers and brewery would then be determined.

## Slide 63: Warehouse and Inventory Level Optimization Study
Safety Stock Data Analysis
A thorough analysis of existing planning and operating systems was conducted.
The model transcended each level of the organization from management to operations to sales therefore data was required for each level of the organization.
Planning forecast and actual production were analyzed including:
  Brewing - Planned and Actual, Linear programming model used in planning
  Production - Planned and Actual, Production Scheduling
  Orders - Planned and Actual
  Wholesaler Sales - Actual
  Wholesaler Inventory Levels - Actual

## Slide 64: Warehouse and Inventory Level Optimization Study
Safety Stock Data Analysis
Data was extracted and tabulated to compare forecasted quantities to actual quantities on a daily basis and was used to minimize large variability and missing data.
Management initiated a corrective action plan for systems based on this analysis.

## Slide 65: Warehouse and Inventory Level Optimization Study
Safety Stock Computations
This was developed as a planning model and management tool.
The statistical analysis to measure variability in manufacturing and sales required an in-depth review and careful consideration to avoid overstating or understating safety stock.
Actual production was plotted against forecast production taking into account the three week time lag between forecasted or planned production and the actual production.
From the plot, one can determine whether a simple linear model is a good choice.
If a linear model is good, it can be fit by using least squares regression and the variability can be estimated by the residual mean square from the fitted regression model.

## Slide 66: Warehouse and Inventory Level Optimization Study
Safety Stock Computations – Calculation Procedure

## Slide 67: Warehouse and Inventory Level Optimization Study

## Slide 68: Warehouse and Inventory Level Optimization Study
Determine the Trade-off Optimal Product Mix
From the analysis of sales and production, the unconstrained safety stocks were determined.
These were the amount to cover variability if there were no limitations on brewing and packaging capacity and constraints of warehouse space.
To determine how and by how much to reduce the theoretical safety stock, an optimal trade-off between the two conflicting objectives, to minimize cost and to minimize stock outages was required.

## Slide 69: Warehouse and Inventory Level Optimization Study
Determine the Trade-off Optimal Product Mix
A Multiple Objective Decision Making Model with constraints was developed to do this.
The model was developed for a one week time period.
The model had brewing, packaging and warehouse constraints and the demand requirements
Demand includes the demand plus the difference in safety stock requirements and beginning inventory.

## Slide 70: Warehouse and Inventory Level Optimization Study
Determine the Trade-off Optimal Product Mix (Form of MODM Model)
Min Stock
-
Outages
Brewing
Packaging
Warehouse
and Sales
Min Cost
$/M BBL
$/Pallet
$/Case
Brewing
>=
Constraints
=
B
ij
<=
Packaging
>=
Constraints
=
P
ij
<=
Warehouse
>=
Constraints
=
W
ij
<=
Product
=
Demand
=
S
ij
=
Optimum
Product
Mix
MODM Model for Optimal Product Mix
Requirement
of products
with safety
stock and
minimum
stocking level.
____________
____________
____________
____________
Given seasonality,
planning period and
promotion effects
Full Goods
Days
Inventory
Capacity
Input from
safety stock
determination
Model will force a minimum
stocking level at the Brewery
and Warehouse
Where
B
ij
,
P
ij
,
W
ij
and
S
ij
=
Brewing, Packaging, Warehouse and
Sales variables (tanks, products,
packaging lines, capacities, etc.)

## Slide 71: Warehouse and Inventory Level Optimization Study
Determine the Trade-off Optimal Product Mix (Form of MODM Model)
Sometimes demand exceeds capacity and no safety stock replenishment can occur and beginning inventory was used to cover it.
The demand in the model was the production requirements which equals the actual demand + safety stock – beginning inventory
Samples were taken from distributions for both the beginning inventory for the wholesaler and warehouse and from the product demand for the aggregate wholesaler.

## Slide 72: Warehouse and Inventory Level Optimization Study
Determine the Trade-off Optimal Product Mix (Form of MODM Model)
Safety stock for the products was selected and production requirements by product and container were computer.
A number of sample points were taken to create the distribution of safety stock that is possible to maintain based on the constraints.
During low demand – all safety stock was produced. During high demand – the MODM model was run to trade-off the objectives
Expected demand plus safety stock was the demand requirement for the week

## Slide 73: Warehouse and Inventory Level Optimization Study
Output of MODM Model – Optimal Strategy

## Slide 74: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift
An expert system was used as a simulation model to track the product through the entire process by shift to determine inventory levels.
This was done for a single week application.
The results from the previous step, the MODM model, was the expected value for the safety stock for each product.
This amount was used in the simulation with random demand samples to generate the distribution of full goods days inventory.

## Slide 75: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift
The expert system had a number of steps involved.
  A random sample of total demand was generated from each wholesaler for a week. (Including the % distribution of products across all wholesalers.)
  The sample demand was adjusted for the safety stock value and run through a LP model to insure no constraints were violated. The single objective of this model was product priority.

## Slide 76: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift
Expert System Steps (continued)
  Given the sample satisfied the constraints, the flow of product by shift is traced through packaging, warehousing and distribution. Methods and rules of operation were modeled including
    Beer availability
    Priority of order
    Assignment to the packaging line
    Line efficiency
    Number of doors and train sidings

## Slide 77: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift
Expert System Steps (continued)
  Inventory levels were captured by product by shift.
  The process was repeated until enough samples were generated to adequately develop the distributions for Full Goods Days Inventory. This included automatically developing of the mean and standard deviation.

## Slide 78: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift

## Slide 79: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift

## Slide 80: Warehouse and Inventory Level Optimization Study
Expert System to Track Process Flow by Shift

## Slide 81: Warehouse and Inventory Level Optimization Study
Sensitivity Analysis
The model integrated a number of different planning and operating systems under one umbrella and took a corporate wide view of operations.
Warehouse requirements, in a sense, are the combination of all other variations in the operating processes
The model was developed as a planning model.

## Slide 82: Warehouse and Inventory Level Optimization Study
Sensitivity Analysis
Types of what-if analysis and parameters that could be changed by the model included:
  Parameters for brewing, lines, shifts, wholesalers and product codes.
  Objective weights
  Capacities and constraints for warehouse, brand, line, brewing duration and product code distribution.
  Historical distributions that had uses in other areas included demand, warehouse beginning inventory, wholesaler inventory and wholesaler sales distributions.

## Slide 83: Warehouse and Inventory Level Optimization Study
Benefits
Insures adequate supply of product to the wholesalers for a growing number of products
Accurately determines the Full Goods Days Inventory needed to provide input on the necessary warehouse space.
Allowed management to determine the optimal amount of inventory to be maintained at both the brewery and wholesaler.
Improves scheduling of brewery and packaging and distribution

## Slide 84: Warehouse and Inventory Level Optimization Study
Benefits
Provides an analysis tool to test changes in the operation before they are put in place to avoid costly errors.
A “predictive model” for determining the optimal inventory level at a brewery.
An interactive tool that allowed management to do “what-if” analysis for changes in operations.
Allowed management to study the impact of introducing new products, changes in operations and changing product demand for wholesalers.

## Slide 85: References
https://www.linearprogramming.info/example-of-a-product-mix-problem-in-linear-programming/
https://www.youtube.com/watch?v=YQgKh1qdFEU
https://www.solver.com/solver-tutorial-solver-model-using-product-mix-example

## Slide 86: References
https://conspecte.com/Supply-Chain-Management/supply-chain-design-and-analysis-models-and-methods.html
http://www.orms-today.org/orms-4-02/frvaluechain.html
https://www.sciencedirect.com/science/article/pii/S037722171300787X
Case Study: Optimization Models in Supply Chain Risk Management
Optimization Methods in Supply Chain Applications: a Review, Conference Paper, Dublin Institute of Technology, Amr Arisha and Waleed Abo-Hamad, 12th Annual Conference of the Irish Academy of Management, Galway Mayo Institute of Technology, Galway, 2-4 September 2009.

## Slide 87: IMSE 802 Supply Chain Operations and Decision Making
Lecture 3
Supply Chain Models